The available info on cabling for the Geneva can be *very* confusing!
The descriptions often conflict with each other, and even the dealers
sometimes don't know what they've got.

Here is a quick rundown as to who's on first, etc.  Where I refer to 
a cable "... terminating in an XYZ connector ...", that refers to the
peripheral end - all the cables have the 8-pin mini-DIN on the computer 
end, of course!  Note, also, that fairly complete info (including pinouts)
is available in the Geneva's Operations Manual.

**********

#723 - terminates in a standard-size 6-pin DIN.  This cable is used to
interface to the P-80, P-80X and P-40 portable printers, as well as the
TF-20 disk drive (a dual 5.25" floppy drive system, AC-powered).

#724 - terminates in a DB-25 connector, and is colored light gray. 
This is a "straight-thru" RS-232 cable, which is used with external
modems (e.g. the CX-20, or Hayes Smartmodem) or any device that follows
DCE ("data set", or modem) type pinouts.

#725 - terminates in a DB-25 as well, but is colored a very dark gray.
This cable is a "null modem" configuration, where certain lines to the
other device are "crossed over" in order to provide the proper
handshaking.  It is used with serial printers, and to hook up to other
computers (e.g. a QX-10 or QX-16, and others) that have a standard DTE
("data terminal") pinout.

#726 - terminates in a mini-DIN on both ends.  This cable is used
primarily for the PF-10 portable 3.5" disk drive, but it can also be
used to hook two Genevas together by their RS-232 or serial ports, for
the purpose of direct communication and data transfer.

**********

Hope this is of some help ...

:: Mike ::
76703,4051