Making BIOS Calls from BASIC on the Geneva



Many people are aware that you can use BIOS operations to give 
BASIC programs some of the power and speed that was formerly 
limited to machine language programs.  Few, however, are aware of 
the techniques required to do this.  In the example program 
below, you will see how a BIOS routine (ADCVRT) can make a BASIC 
program more powerful and read the internal and external 
voltages.

Learning how to use BIOS calls can be very useful for new 
programmers.  It allows them the ease and simplicity of writing 
in BASIC and then reverting to the more difficult machine code 
only when specialty problems of speed or power arise.  The end 
result can be powerful programs written with ease.  Some knowledge 
of machine code and operating systems is required.  


General Procedure

You begin by writing your program in BASIC, leaving the machine 
portion undone.  When you are satisfied that all the BASIC 
keyboard I/O routines, menus, etc. are in working order, you can 
develop the machine code portions that will give you the 
additional power.  


Developing the Machine Language Portion

Here is the sequence of tasks the machine language portion must 
accomplish to handle a BIOS call and pass the results back to 
BASIC:
 
1.  Discover the warm boot address.

2.  Add a certain number to it to call the particular BIOS 
    routine.  Each BIOS routine you call requires a different 
    number to be added to it to address that routine.

3.  Store this updated address to memory.  The stored address 
    (which is the sum of the WBOOT address and an added offset) 
    equals the calling address of the desired BIOS routine. 

4.  Call the desired BIOS routine (in the example below it reads 
    voltage through the A/D port). 

5.  Return to the BASIC program where the data retrieved from 
    the called routine is converted to meaningful numbers to be 
    displayed on the screen. 

The machine language program that does this is shown below.

Once the machine language program is developed, a couple more 
steps remain.  The machine language op codes must be be converted 
to decimal codes.  Finally, the converted machine language (now 
in decimal format) must be inserted into upper memory (usually 
the USER BIOS area) with POKE statements assisted by READ/DATA 
statements. 

If you choose the USER BIOS area to write your machine code 
portion in, you must set aside enough room with the CONFIG 
program.  Since the machine program is less than one page of 256 
bytes in the example program, the USER BIOS is located at hex 
address EB00.  If the routine were more than one page, the 
starting address would move down one page for each page of code.  
For example, a two page routine would have to start at hex 
address EA00.

WARNING: Do not attempt to measure A.C. voltages of any 
magnitude or D.C. voltages greater than 2 volts.  You can 
seriously damage the Geneva if you try to do this.


Sample Program that Reads the Geneva Battery and External 
Voltages

10 REM This is a program to read internal battery voltages and
       external D.C. voltages up to 2 volts.
20 REM It is written in BASIC, but it calls machine language 
       routines in the USER BIOS.
30 CLS
40 IF PEEK(&HF00B)<>1 THEN PRINT "USER BIOS SIZE IS NOT 1 BLOCK--
   USE CONFIG PROGRAM TO CORRECT THIS: SET TO 1 PAGE.":END
50 INPUT "DO YOU WANT TO READ INTERNAL BATTERY OR EXTERNAL
   VOLTAGES(B/E)";V$
60 IF V$="E" THEN GOTO 300
65 IF V$="B" THEN 90
70 PRINT "USE CAPITALS -- ENTER B OR E"
80 GOTO 50
90 REM *** SECTION TO DEFINE INITIAL VALUES ***
100 DEFINT A-J,L-Y
110 K=5.7/63             'DIVIDE 5.7 V INTO 64 PARTS FOR INTERNAL
120 Z=2/64
130 ADRS=&HEB00                         'USER BIOS AREA
140 T=0
150 REM *** SECTION TO POKE MACHINE CODE DATA TO DISK ***:
160 FOR I=&HEB00 TO &HEB17:           'THIS IS THE USER BIOS AREA
170 READ A
180 T=T+A
190 POKE I,A
200 NEXT I
210 IF T<>2362 THEN PRINT "ERROR IN DATA LINES!!!!":END
220 IF V$="E" THEN POKE &HEB0B,0
230 REM *** SECTION TO CALL ROUTINE AND CONVERT DATA ***
240 CALL ADRS
250 X=PEEK(&HEB17)      'GET THE STORED NUMBER THAT = VOLTAGE NUM
260 PRINT "NUMBER RETURNED FROM A TO D PORT=" X
270 IF V$="E" THEN PRINT X*Z "VOLTS" ELSE PRINT X*K "VOLTS"
280 END
290 REM EXTERNAL VOLTAGE SECTION
300 CLS:PRINT "NEVER EXCEED 2 VOLTS - USE D.C. VOLTAGES ONLY****"
310 PRINT "ACCURACY LIMITED TO 6 BITS (=1 PART IN 64)"
320 PRINT:PRINT "HIT ANY KEY WHEN READY TO PROCEED"
330 INPUT Z$
340 GOTO 90
350 DATA 42,1,0,125,198,111,111,34,13,235,14,3
360 DATA 205,114,231,31,31,230,63,50,23,235,201,61


Detailed Look at the Machine Code Portion

EB00 LHLD      0001      2A,01,00            42,1,0
EB03 MOV       A,L       7D                  125
EB04 ADI       6F        C6,6F               198,111
EB06 MOV       L,A       6F                  111
EB07 SHLD      EB0D      22,0D,EB            34,13,235
EB0A MVI       C,03      0E,03               14,3,     
EB0C CALL      EA72      CD,72,EA            205,114,231
EB0F RAR                 1F                  31     
EB10 RAR                 1F                  31
EB11 ANI       3F        E6,3F               230,63
EB13 STA       EB17      32,17,EB            50,23,235
EBI6 RET                 C9                  201

The Geneva will read voltages internal and external if the ADCVRT 
BIOS function is called.  To call it, you must know the address 
where this routine resides.  The address is equal to the warm 
boot address plus the hex number 6F.  So the operation of reading 
voltages takes place in these steps.

In all CP/M machines, the warm boot address can always be located 
by reading the data stored in locations 1 and 2.  A 16-bit read 
instruction will read both locations at once, and store the warm 
boot location in the HL register if this instruction is:

  LHLD 0001

The LHLD instruction causes the 16-bit read that reads both 
addresses.  The 0001 gives the starting address 1.  The WBOOT 
address has now been read from locations 1 and 2.

Next, addition cannot be done in the HL register, so the data 
stored there must be moved from the HL (called L below) to the 
accumulator (called A below).  All addition is done in the 
accumulator.  This move operation is done with the instruction:

  MOV A,L 

Now that the warm boot address has been moved to the accumulator, 
the next step is to add hex number 6F to it with this 
instruction:

  ADI 6F

The first stage is now done.  The number in the accumulator 
represents the address of the BIOS routine that calls the ADCVRT 
routine.  We must store this number for future use.  This magic 
number is stored back to the HL register with the command: 

  MOV L,A

Finally, the number must be stored one more time in a permanent 
memory location so it can be called when needed.  It is done in 
this program with the command:

  SHLD EB0D
 
Now that the address to call has been determined and stored at 
the address directly after the CALL instruction, the next step is 
to determine whether the voltage read will be an internal 
voltage (battery voltage) or an external voltage.  To make this 
choice, a certain number must be placed in the C register just 
prior to calling the voltage reading routine.  In the example 
below, the internal battery voltage is read by placing a 03 
into the C register with the instruction:

  MVI C,

At this point all the preliminary work has been done and it is 
time to call the routine that will read the voltage.  Calling 
this routine will leave a number in the accumulator that 
represents the voltage read.  This number will be from 0 to 63. 

If you place a 03 in the register before calling the routine, 
you read battery voltage.  Each of the 64 numbers in the 
accumulator represents the battery voltages from 0 to 5.7 in 64 
steps.

If you had placed a 0 in the C register before calling the 
routine, each of the 64 numbers you find in the accumulator 
represent external voltages from 0-2 V.D.C. in 64 steps. 

At this stage all preliminary work has been done.  All you need 
to do now is call the routine.  This is done with the command:

  CALL EA72

NOTE: The EA72 is a dummy address; it is replaced by the data 
provided by the SHLD instruction above.

The Voltage has been read by calling the ADCVRT routine, but the 
number stored is an 8-bit value and the port is only capable of 
reading with 6 bits of accuracy.  So only 6 of the 8 bits read 
have useful information.  To eliminate the right two useless 
bits, you issue rotate right commands like this:

  RAR
  RAR

Masking is performed to get rid of any useless carry bits that 
may have crept in from the left.  This is done with the command:

  ANI 3F

The final results are now stored at a safe location waiting for 
BASIC to read and convert it.  This is done with the command:

  STA EB17

You have now found the location, called the routine, read the 
data, removed the useless portions and stored the results.  The 
final step is to return to BASIC.  This is done with the command:

  RET

By multiplying a compensation factor by the number you stored, 
BASIC can now read voltages with an accuracy of 1 part in 64. 


Notes on Using the ASM Program

The machine program shown must be processed by the ASM program to 
generate the hex file that will be used.  Before the ASM program 
can use the machine file, certain alterations must be performed.  
First, a starting address is needed for the ORG statement.  Since 
you are using a one-page USER BIOS, the program is ORGed 
(started) at EB00.  Next, the assembler requires that all hex 
numbers end with the letter H.  An example of how this looks when 
completed is shown below. 

  ORG       0EB00H
  LHLD      0001
  MOV       A,L
  ADI       6FH
  MOV       L,A
  SHLD      0EB03H
  MVI       C,03H
  CALL      0EA72H
  RAR       
  RAR
  ANI       03FH
  STA       0EB17H
  RET	


Using the HEX file

When the ASM program has processed your source machine code file, 
it produces two new files: one with a .HEX extension, and one 
with a .PRN extension.  It is the .HEX one that you need to get 
the HEX codes necessary to convert into your BASIC program.  The 
HEX file looks like the one shown below:
 
  :10EB00002A01007DC66F6F2203EB0E03CD72EA1F50
  :07EB10001FE63F3217EBC9BD
  :0000000000

There is definite order to this seeming madness.  As you can see 
by looking at the the organized version below, the first portion 
is starting line numbers and addresses.  This is followed by the 
actual data.  The last part of each line is a checksum digit to 
insure accuracy.  The file is terminated by a line of zeros 
instead of the usual control Z.  The only part that is useful is 
the 16 pairs of numbers on each line (separated by parentheses in 
the example below).  These are the number pairs that are 
converted to decimal and POKEd into upper memory to form the 
machine language part of the program.

:10  EB00 00   (2A 01 00 7D C6 6F 6F 22 03 EB 0E 03 CD 72 EA 1F) 50
:07  EB10 00   (1F E6 3F 32 17 EB C9) BD
:0000000000

The Hex pairs of numbers can be converted in BASIC by using the 
PRINT command with the &H prefix.  For example, to convert the 
first two pairs on hex numbers above you would enter:
   
  PRINT &H2A
  PRINT &H01

The computer would return these values (in BASIC):

  42
  1

By repeating this sequence, all of the hex data pairs can be 
converted to decimal numbers to be poked into the upper memory or 
the USER BIOS area. 

There is a simpler way to directly insert the hex data into upper 
memory.  The DDT program will automatically load the file into 
upper memory if the file has been given a starting address with 
the ORG command.  This is done by entering a statement like this:

  DDT FILE.HEX