ADDRESSES FOR GENEVA INTERRUPT ROUTINES

                         by Justin Bell


Routines  to  handle interrupts for the Geneva should  always  be 
written above 8000 hex as one user recently found out.   He wrote 
a  routine to handle the interrupt generated by the free  running 
counter and located this routine in the 1st page of the TPA area.  
He  had checked his routine again and again for correctness,  but 
the  routine  would  always blow up.   Baffled,  he  called  Tech 
Support for help.

The problem was caused by the bank swiching nature of the Geneva.  
The  1st  32K (0 to $7FFF) of the   Geneva's memory exists in two 
different  places.   There is a 32K bank of RAM and a 32K bank of 
ROM.   During  normal  program operation,  the 32K  bank  of  ram 
memory is active.   However, the Geneva swithces over to the ROM 
bank in these three cases:

     1. During initial boot up.
     2. Whenever BIOS or BDOS calls are being executed.
     3. Whenever an interrupt is generated.

Since  the  user was calling his routine when  an  interrupt  was 
generated  by  the  free running counter,  the Geneva  would  not 
execute  the  users  routine he had so neatly written  into  RAM.  
Instead  the Geneva would bank switch over to the ROM  bank  and 
try  to execute who-knows-what code that was in the same  address 
of the ROM bank.  The obvious result was binary bafflement.

Moral:  Write routines for interrupt handling above 8000 hex.  An 
excellent place is the user BIOS area which always ends a address 
EBFF  hex.   See  the technical note below to see where the  USER 
BIOS starts. 

See  appendix  C  of  the SYSTEMS ESSENTIAL manual  for  a  brief 
explanation of how to use interrupts with the function keys.     

TECHNICAL NOTE: 

The  Starting address of the USER BIOS area varies with the  size 
set with the CONFIG program.  It starts at EB00 when the size  is  
one page but, the starting address moves downward as the size  is 
increased.  Example:


# of pages         start address       end address

1                   $EB00               $EBFF
2                   $EA00               $EBFF
3                   $E900               $EBFF
4                   $E800               $EBFF
5                   $E700               $EBFF